## Slide 1: Ch.4.
Acid Mines Drainages (AMD)
  Exposure of the reduced minerals by mine excavating
  Oxidation of the reduced minerals producing acids
  Pyrite is the primary source of the acid

## Slide 2
  Pyrite
    FeS2
    Most frequently observed sulfide in crust
    Oxidized to produce acid, causing severe environmental problems such as AMD and acid rain
http://mineralminers.com/html/pytmins.stm

## Slide 3
  Pyrite Oxidation
    Complex multistep process (Luther, 1997; Rimstidt and Vaughn; 2003)
    Microbial vs. abiotic
    Bulk reaction pathways:
      FeS2 + 3.5O2+H2O = Fe2+ + 2SO42-+2H+ (R1)
      FeS2+14Fe3++8H2O = 15Fe2++SO42-+16H+ (R2)
      Fe2++0.25O2+H+ = Fe3++0.5H2O (R3)
    Dominated by microbial oxidation in nature

## Slide 4
Microbes capable of oxidizing pyrite

## Slide 5
  Acidithiobacillus ferrooxidans
    (Old name: Thiobacillus ferrooxidans)
    Gram negative acidophillic chemolithoautotroph

## Slide 6
Imgok Creek, Imgok, Korea 1996

## Slide 7
http://wiki.biomine.skelleftea.se/wiki/index.php/Image:AMD_in_Rio_Tinto_river.jpg
Rio Tinto, Spain

## Slide 8
  Environmental Impacts by AMD
    Atheistically bad due to the precipitation of Fe-oxyhydroxides
    Degrading water quality and limiting water resources due to
      Low pH
      High concentrations of toxic metals
      Lack of O2
      Turbidity & coating by the Fe-ppts
    Destruction of water ecosystem

## Slide 9
  Treatment of AMD
    Active
      Physical:
        Aeration
        Bubbling
        Mechanical mixing
      Chemical:
        Oxidation
        Dissolution
        Neutralization
      Biological
        Accelerating the oxidation
        Prohibiting the oxidation
    Passive
      Swamp
      Reactive beds

## Slide 11
http://pruned.blogspot.com/2008/02/treating-acid-mine-drainage-in.html
Treating Acid Mine Drainage in Vintondale

## Slide 12: Ch.4.
Other Environmental Problems in Mining Area
  Noises
  Dusts
  Accidents
  Subsidence

## Slide 13
From http://www.graphicshunt.com/health/images/black_lung-577.htm
Black Lung

## Slide 14
From http://www.courier-journal.com/cjextra/blacklung/graphics/diseasedlung.html

## Slide 15
From http://www.cdc.gov/niosh/programs/mining/risks.html

## Slide 16
From http://www.donga.com/fbin/output?n=200805240249
Subsidence in Eumsung, Choongcheongbukdo, May 24, 2008